Project Outline

Wu Jingyan

Project name: Hand-Eye Calibration

Project Supervisor: Yuan Qilong, Ivan Sim

Creation date: 9th Jan

Project Summary

In recent years, with the popularization of robotic industry, the deviation of the dimensions from the vision-operated robots has become a major problem for the accuracy of the measurements.

In this project, the calibration of the video camera on robot’s manipulators based on a relative positioning method has been under investigation for a need of more accurate measurements so that further calculations can be correctly carried on.

The functionalities of ROS, Rviz and Gazebo were explored for robot application construction, path planning and real-world simulation. The utilization of camera plugin, OpenCV, broadcaster-listener, spherical sampling, inverse-kinematic and rosbag method in programming to help achieve the functions of camera mounting, marker identification data transmission, geometric calculation correspondingly. The automation of the whole circle of sampling and calibration procedure was achieved.

Assumptions & Constraints

The assumptions and constraints below were made for the ease to complete the project.
1. The numbers measured manually for various kinds of physical quantities is accurate.
2. The marker is always centralized at the given position and orientation.
3. The positions and motions of the robot are constrained above the table surface.

Programming language

Python and C++ were used as the programming language of the project because they both adapts OpenCV well and generally proceed faster. In comparison, OpenCV combines the advantages of both languages, in which Python that is simple for programmers are run under C++, which is then more understandable for the computers.

Environment setup

The environment was established by importing the URDF file to generate an environment with a mechanical arm UR5 mounted with a video camera, aruco marker and a simulating table. Simultaneously, collisions were disabled in SRDF file to avoid redundant judgments of collision and enable the system’s operation.

Actuation procedure

I. Robot kinematics modeling with URDF (explain the concepts)
URDF (Unified Robot Description Format) is a markup language used to describe the physical and geometric properties of robots. It is commonly used in robotics to model the kinematics of robots, which involves describing how the different parts of a robot move relative to one another.
In this experiment, UR5 robot was used as the testing prototype. In URDF, robots are typically represented as a hierarchy of links and joints. A link represents a rigid body of the robot, while a joint represents a connection between two links that allows them to move relative to one another. There are several types of joints that can be used to model different types of motion, such as revolute joints (which allow rotation about a fixed axis) and prismatic joints (which allow translation along a fixed axis).
To model the kinematics of a robot using URDF, the different links and joints that make up the robot were firstly defined. Each link is defined by its visual and collision properties (such as its shape, size, and mass), as well as its relative position and orientation with respect to its parent link. Each joint is defined by its type, axis of rotation or translation, and its limits (such as its maximum and minimum angle or distance). A picture is shown as below, which demonstrated the relationship among UR5, the joints and links.
Once the links and joints were all defined, URDF could be used to compute its forward kinematics, which involves computing the position and orientation of the end-effector (the tool or device attached to the robot) given the joint angles or positions. The inverse kinematics of the robot could also be computed with URDF, which involves computing the joint angles or positions needed to achieve a desired end-effector position and orientation.
Overall, URDF provides a flexible and powerful way to model the kinematics of robots, which is essential for many applications in robotics, such as robot control, simulation, and path planning.

II. Setup of motion planning software (MoveIt!)
i. MoveIt! could be installed by the following command:
sudo apt-get install ros-noetic-moveit
ii. Additional dependencies were installed with the following command:
sudo apt-get install ros-noetic-moveit-*
iii. MoveIt! package dependencies were added to ‘package.xml’ file so that MoveIt! with robot model UR5 could be used.
iv. A configuration package was created using ‘moveit_setup_assistant’ tools with the following command:
rosrun moveit_setup_assistant setup_assistant
- In the "Robot Model" section, ‘UR5.URDF’ was used.
- URDF file was parsed and a visual presentation was generated by MoveIt Setup Assistant.
- A MoveIt configuration package was generated after the configuration of robot model.
- The package was built with catkin build.
- The followed command was used to launch MoveIt and achieve robot visualization.
roslaunch ur5_moveit demo.launch

III. Setup of Gazebo Simulator (Robot, cameras, markers etc)
- Gazebo was launched and the robot simulating was on procedure with the above command “roslaunch ur5_moveit demo.launch”.
- For mounting camera on the robot, the Gazebo camera plugin was added to ur5’s urdf, as in the following tutorial:
https://classic.gazebosim.org/tutorials?tut=ros_gzplugins
- Github resources of markers was added to the package as the models
(https://github.com/joselusl/aruco_gazebo)
then, the markers were inserted to the Gazebo world file, such that Gazebo can simulate the markers.
IV. Aruco marker tracking
- The functions of OpenCV were implemented to achieve detection and identification of the markers.
- The detection and identification was done using “aruco::detectMarkers” function.
- The “aruco::estimatePoseSingleMarkers” function gives us the estimated pose of the marker.
V. Robot pose sampling method for calibration pose selection
- During the robot pose sampling, the robot was moved to a number of different poses with the pose data recorded. The poses should be ensured that the camera can see and identify specific marker. Points that cannot see marker should be filtered. Thus, spherical sampling method was applied around specific marker.
- Random sampling of the points on the sphere of marker center origin was used as the method.
- Eigen::Matrix3d library was used for frame conerting.
VI. Robot inverse kinematics based on TF assistant
- To achieve a desired end-effector pose, the corresponding joint angles were
computed based on robot inverse kinematic process.
- Multiple coordinate frames over time were tracked by TF (transform) assistant, which is a GUI tool in ROS that helps the transformation tree visualization and debugging.
- A kinematic model in ROS was created with a robot state publisher node.
- TF assistant tool was applied to visualize the transformation tree of the robot.
- A desired end-effector(tool_0) pose related to the base of the robot(base_link) was defined in the TF Assistant tool.
VII. Calibration method description
- Calibration data was collected by moving the robot to a set of known poses as stated above and recording the corresponding end-effector positions and joint angles.
- A cost function of the calibration parameters that measured the difference between the predicted positions and the observed end-effector positions was defined based on the robot kinematic model.
- The calibration parameters were estimated based on evenberg-Marquardt algorithm / Gauss-Newton algorithm optimization algorithm for cost function minimization and calibration parameter estimation.
- Calibration was validated by moving the robot to new poses and comparing the predicted and actual end-effector positions based on the calibrated kinematic model. As this done, the whole procedure of calibration has been completed.

Resources:
The entire code can be found on the Github: Jingyannnn/ur5_moveit (github.com)