Project Outline

Wu Jingyan

Project name: Hand-Eye Calibration

Project Supervisor: Yuan Qilong, Ivan Sim

Creation date: 9th Jan

Project Summary

In recent years, with the popularization of robotic industry, the deviation of the dimensions from the vision-operated robots has become a major problem for the accuracy of the measurements.

In this project, the calibration of the video camera on robot’s manipulators based on a relative positioning method has been under investigation for a need of more accurate measurements so that further calculations can be correctly carried on.

The functionalities of ROS, Rviz and Gazebo were explored for robot application construction, path planning and real-world simulation. The utilization of camera plugin, OpenCV, broadcaster-listener, spherical sampling, inverse-kinematic and rosbag method in programming to help achieve the functions of camera mounting, marker identification data transmission, geometric calculation correspondingly. The automation of the whole circle of sampling and calibration procedure was achieved.

Assumptions & Constraints

The assumptions and constraints below were made for the ease to complete the project.
1. The numbers measured manually for various kinds of physical quantities is accurate.
2. The marker is always centralized at the given position and orientation.
3. The positions and motions of the robot are constrained above the table surface.

Programming language

Python and C++ were used as the programming language of the project because they both adapts OpenCV well and generally proceed faster. In comparison, OpenCV combines the advantages of both languages, in which Python that is simple for programmers are run under C++, which is then more understandable for the computers.

Environment setup

The environment was established by importing the URDF file to generate an environment with a mechanical arm UR5 mounted with a video camera, aruco marker and a simulating table. Simultaneously, collisions were disabled in SRDF file to avoid redundant judgments of collision and enable the system’s operation.

Actuation procedure

I. Camera mounting

II. Marker identification & pose publication

III. Sampling

IV. Data storage

Resource requirement